## Slide 1: Compiled Once. Published Once. Mounted Everywhere.
CernVM-FS, the Compute Canada model, and EESSI - how scientific software actually reaches the machines that run it ndexr.io

## Slide 2: Part I - The problem nobody funds

## Slide 3: Enterprise Linux is old on purpose
Your cluster runs an enterprise distribution because the vendor supports the interconnect, the parallel filesystem and the GPU driver against that kernel and no other. The cost is a frozen userland.
Distribution | Kernel | GCC | glibc | Python
RHEL / Rocky 8 | 4.18 | 8.4 | 2.28 | 3.9.2
RHEL / Rocky 9 | 5.14 | 11.2.1 | 2.34 | 3.9.10
Fedora 41 | 6.11 | 14.2.1 | 2.40 | 3.13.0

## Slide 4
The first two rows are what you run. The third is what your users’ documentation assumes.

## Slide 5: So everybody installs everything, everywhere
The user’s move fails - sudo dnf install ... on a login node, and the sudoers lecture
The administrator’s move does not scale - one modulefile, then another version, then a second compiler, then a third MPI. All written by hand.
And the site next door is doing it too - same packages, same sources, different results
The effort is real, the people are good, and almost all of it is duplicated.

## Slide 6: The axis is not build-or-mount

## Slide 7
It is how many times. The tree gets built either way.

## Slide 8: The four requirements, written before the tools
Users should be presented with an interface that is as consistent and as easy to use as possible across all sites. It should also offer optimal performance.
— Digital Research Alliance of Canada
A way to distribute it → CernVM-FS
Independence from the host OS → a compatibility layer
Automated installation - humans are not consistent → EasyBuild
An interface that survives ten thousand combinations → Lmod, hierarchical

## Slide 9: “Isn’t this what containers are for?”
Two things the word reproducible is doing at once:
Repeatability - running the same bits again. Containers are excellent at this.
Accountability - saying what those bits are. A container cannot touch it.
A container is a distribution format, not a derivation. Freezing an unknown does not make it known.

## Slide 10: And, separately, the practical failure
The image grows with the catalogue - the unit of change is the whole image, not the package
You ship what might be used, not what is - importing one Python library touches ~3,500 files out of hundreds of thousands
Containers stay in the picture. They carry an OS and a mount point, not a stack.

## Slide 11: Part II - The delivery substrate

## Slide 12: CernVM-FS: software, streamed
A read-only directory under /cvmfs that behaves like an on-demand streaming service. Nothing installed, nothing downloaded up front - files arrive when a process opens them.
A filesystem, not a package manager - FUSE, so every tool that opens a file can use it
Content-addressed - identical bytes stored once, everywhere
Compressed on the server, transparent on the client
Ordinary HTTP - the cache is Squid, the mirror is Apache

## Slide 13: Integrity: one signature, covering everything

## Slide 14
Exactly one object is signed. Everything else is reachable from it by content hash.

## Slide 15: The manifest is the entire entry point
C7d1e... # root catalog, by content hash B1179648 # its size in bytes Xf3a9... # hash of the signing certificate T1747526400 # when this revision was published D240 # how long a client may cache it S5348 # revision number Nsoftware.eessi.io # fully qualified repository name -- # everything below is the signature
The transport does not need to be trusted. A proxy, a mirror or a disk can be wrong without the client being wrong.

## Slide 16: Publishing is a transaction
cvmfs_server transaction software.example.org # ... install ... cvmfs_server publish -a r-4.5.1 -m 'R 4.5.1, foss/2023a' software.example.org cvmfs_server abort software.example.org # throws it all away cvmfs_server rollback -t r-4.5.1 # go back to a named revision
Every publish is an immutable revision. There is no half-published state for a client to catch.

## Slide 17: Four tiers, and what each one is for

## Slide 18: Sizing, in one slide
Stratum 0 - the only writable copy. Small, controlled, not load-bearing for readers.
Stratum 1 - full replica. Private one ≈ 360 GB for EESSI, +1 GB/day. Your disconnect insurance.
Proxy - one per 100-500 nodes, at least two. This is what makes MPI start-up bearable.
Client cache - on the SSD, big enough. Where almost every read is answered.

## Slide 19: The entire client configuration
# /etc/cvmfs/default.local CVMFS_HTTP_PROXY="http://proxy-a:3128|http://proxy-b:3128" CVMFS_QUOTA_LIMIT=10000 # 10 GB of local cache CVMFS_CACHE_BASE=/ssd/cvmfs # the fastest disk the node has sudo cvmfs_config reload ls /cvmfs/software.eessi.io # mounted on demand by autofs

## Slide 20: What it scales to (CERN, May 2026)
~15 Stratum 1 mirror servers
> 33 billion files in the /cvmfs tree
~2 PB accessible - proven to 100 PB
~290 repositories, including 8,000+ container images

## Slide 21: It is faster than the filesystem you already own
Importing one Python package touches ~3,500 files / ~1.1 GB, most of them tiny.
Where the software lives | Time to import
Local SSD or ramdisk | ~2 s (the floor)
GPFS / Lustre | 30-60 s, even with a hot pagepool
CernVM-FS, cold cache, near Stratum 1 + proxy | dramatically better
CernVM-FS, warm client cache | approx. local disk

## Slide 22: Why: only the closure crosses the wire

## Slide 23
The catalogue grows without bound because nothing pays for the parts it does not open.

## Slide 24: Part III - One architecture, two implementations

## Slide 25: Four layers

## Slide 26: …and the middle one is a role, not a product
Canada filled the compatibility slot with Nix
Canada then replaced it with Gentoo Prefix
EESSI chose Gentoo Prefix from the start
Three configurations, two programmes, one working architecture each time - and the layers above and below did not change when it was swapped.
This converts a technology bet into an architectural choice.

## Slide 27: The compatibility layer
A full OS userland installed somewhere other than / - its own loader, glibc, coreutils, bash, autotools - built from source, without root.

## Slide 28: Why Nix was replaced, in their words
Store hashes leaked upward through CMake, qmake and Python virtualenvs
Garbage collection was destructive - the feature, from the other side
Gentoo Prefix: no symlinks, no store leak, minimal solution.
— Digital Research Alliance of Canada, on the 2020 migration

## Slide 29: What it actually costs to run a prefix
Downloaded binaries need patchelf --set-interpreter
A stale LD_LIBRARY_PATH=/usr/lib64 in a .bashrc breaks most tools
Anaconda and Julia ship binaries that do not always work - hence 17,000+ wheels
$EPREFIX/var versus /var - who and last read an empty file
One central libstdc++, so GCCcore builds collapse to one module level
Every site hits these in the same order. That is a much better position than a set nobody has written down.

## Slide 30: EasyBuild records it

## Slide 31
The easyconfig is copied into the installation. Provenance is a by-product, not a chore.

## Slide 32: Lmod makes it choosable

## Slide 33: Architecture belongs in the hierarchy, not the name
$ module load fftw Lmod has detected the following error: These module(s) exist but cannot be loaded as requested: "fftw" $ module spider fftw/3.3.10 You will need to load all module(s) on one of the lines below first: gcc/12.3 openmpi/4.1.5 $ module load gcc/12.3 openmpi/4.1.5 fftw/3.3.10
~1,000 applications × 4 CPU generations × 4 GPU generations = 10,000+ permutations. The user sees fftw/3.3.10.

## Slide 34: The Canadian stack, in numbers
5 regional consortia, 38 institutions, ~18,000 accounts, 6 national systems
~1,000 scientific applications, 10,000+ version/CPU/toolchain permutations
17,000+ Python wheels
One catalogue, one scheduler, one way of installing things - since 2017

## Slide 35: Getting in
# the Alliance stack - public, mountable anywhere source /cvmfs/soft.computecanada.ca/config/profile/bash.sh module load StdEnv/2023 # EESSI - in the default CernVM-FS config since November 2023 source /cvmfs/software.eessi.io/versions/2023.06/init/bash module load R/4.3.2-gfbf-2023a

## Slide 36: Old environments stay mountable
Environment | Compiler | MPI | What changed
StdEnv/2016.4 | GCC 5.4 / Intel 2016.4 | OMPI 2.1.1 | First unified environment
StdEnv/2018.3 | GCC 7.3 / Intel 2018.3 | OMPI 3.1.2 | First AVX-512
StdEnv/2020 | GCC 9.3 / Intel 2020.1 | OMPI 4.0.3 | Nix → Gentoo Prefix
StdEnv/2023 | GCC 12.3 / Intel 2023.1 | OMPI 4.1.5 | GCC default; min AVX2; FlexiBLAS; CUDA 12

## Slide 37: Nothing is promoted by being edited

## Slide 38
Already a qualification pipeline, whether or not anyone calls it one.

## Slide 39: EESSI: the same architecture, new hardware
Architecture | Targets
x86_64 / AMD | zen2, zen3, zen4, zen5
x86_64 / Intel | haswell, skylake_avx512, cascadelake, icelake, sapphirerapids
aarch64 | neoverse_n1, neoverse_v1, a64fx, nvidia/grace
riscv64 | separate development repository

## Slide 40
Validated with a ReFrame test suite a site runs against its own mount.

## Slide 41: The tree carries all of them; the machine picks

## Slide 42
“We moved to Arm” stops being a recompile and a revalidation.

## Slide 43: The seam: host injections

## Slide 44
CUDA’s licence permits redistributing runtime libraries only - so nvcc is a symlink into a local SDK.

## Slide 45: …and the influence now runs both ways
The Alliance’s Gentoo Prefix bootstrap is based on EESSI’s Ansible implementation
The Alliance has adopted EESSI’s variant-symlink approach for CUDA driver libraries
The method has transferred between programmes that share no staff, funding or hardware - and is now transferring back.

## Slide 46: Part IV - Running it

## Slide 47: What you actually stand up, in order
Client - a package, a public key, a config file. autofs mounts on demand.
Two proxies, once you have nodes - one per 100-500 workers
A private Stratum 1, if a lost link would stop work - one replica, one Apache, one cron job
Diskless nodes - a loopback file on the shared filesystem, sized ~15% above the cache
Monitor two things - cache cleanup frequency, and client revision versus Stratum 1

## Slide 48: The four error messages, decoded
What it says | What it means
Too many levels of symbolic links | Mount namespace not shared. Almost always a container.
No such file or directory | A catalog could not load. The reason is in the syslog.
Transport endpoint is not connected | The client died and the watchdog did not restart it.
Software caused connection abort | The kernel cut the FUSE connection. Remount.

## Slide 49: Five commands worth knowing first
cvmfs_config probe software.eessi.io # is it reachable at all cvmfs_config stat -v software.eessi.io # revision, cache use, hit rate cvmfs_config showconfig software.eessi.io # what it thinks it was told cvmfs_talk -i software.eessi.io ncleanup24 # cache evictions in 24h sudo cvmfs_config wipecache # last resort, not first

## Slide 50: The boundary - what this does not solve
Updates are visible within minutes, not instantly
The signing whitelist expires - an availability dependency on the runbook
Unprivileged mounting works, but each process gets its own cache
EasyBuild does not sandbox - bit-for-bit is a target, not a guarantee
Licensed software does not fit the model
Derivation proves construction, never meaning

## Slide 51: The one that catches people
If your nodes have no local disk, do not run one client and export it over NFS.
It can be made to work. It is slow. It generates more operational problems than any other configuration in the deployment guidance.
Use a loopback cache file on the shared filesystem instead.

## Slide 52: Part V - What it settles

## Slide 53: Four questions that stop being open

## Slide 54: Consequences, not benefits
“Which version is this?” has one answer - same source, same compiler, same BLAS, same bytes
Approval attaches once, on the trunk - a second approval path is two things to keep in agreement forever
Reproducing an old result is a mount, not a rebuild
Changing architecture stops being a project - Arm is the same line resolving elsewhere

## Slide 55: Where this leaves us
None of this is novel and all of it is in production, at national scale, for around eighteen thousand researchers.
The useful conversation is not whether the model works - two national programmes have answered that - but which parts of it fit the estate you already have.
https://what.ndexr.io